## Slide 1: Robot car workshop
by Domokos Kertész

## Slide 2: Goal
Understand the basics
Move
Avoid crash
Create custom stuff with the car
Tools for more building

## Slide 4: Electricity
A – current (amps) – how many flows
V – voltage (potential difference) – that’s why it flows
R – resistance (ohm Ω) – that’s why it slows
Flow of electrons.
Notes: Voltage is like a slope

## Slide 5: Electrical components
Resistor
Capacitor
LED
Potentiometer

## Slide 6: What is a microcontroller
MCU
  Processor cores
  Memory
  I/O
  RAM
Embedded applications

## Slide 7: What will we use?
Development board
MICROCONTROLLER
USB controller
CLOCK
Pinouts (pin)

## Slide 8: Arduino
Open-source hardware company
Qualcomm exit
ATMEL based boards
  UNO
  Leonardo
  Nano

## Slide 9: Arduino nano
ATmega328/ATmega168
Program memory size: 16kB
Data RAM: 1kB
Clock frequency: 20MHz
ROM size: 512B
Chinese clone

## Slide 10: Arduino nano
Pinouts
PWM
Analog IN

## Slide 11: Interface – Arduino IDE
Interface for programming
  Lightweight IDE
  Build system
  Upload system
Different hardware different architecture
  arm-gcc, avr-gcc
#include <Arduino.h>

## Slide 12: Async communication protocols

## Slide 13: Interface – serial communication

## Slide 14: PWM – pulse width modulation
We can’t do analog
Let’s fake it!
(motors can’t take it)

## Slide 15: Motor controller

## Slide 16: Microservo motor
Angle
PWM

## Slide 17: Breadboard

## Slide 18: Programming basics
Variable (has a type and a value)
Function (has input(s) and output(s))
Syntax
  close everything [{(
  ; after every line
  Space doesn’t matter (if it’s not inside a word)
Neither enter

## Slide 19: Arduino functions
void setup() – once on every start
void loop() – runs constantly
delay([waiting in ms]) – waits till the parameter
pinMode(pin, OUTPUT/INPUT) – sets a pin in/output
digitalWrite(pin, 1/0) – turns in or out a pin
analogWrite(pin,0-255) – writes a PWM signal

## Slide 20: PWM – pulse width modulation
We can’t do analog
Let’s fake it!
(motors can’t take it)

## Slide 21: First code – blink a LED

## Slide 22: Make the wiring!
Do not connect – and +
GND and 5v
GND and 3v3
GND and VIN
OR

## Slide 23: Wire up!

## Slide 25: Servo functions
Connect to a PWM pin (and + & -)
# include <Servo.h>
Servo myServo(pinNumber)
myServo.write(angle)

## Slide 26: If we have time… Overviews

## Slide 27: CAD design
Onshape -> web-based CAD software
https://cad.onshape.com/signin

## Slide 28: Electrical design
KiCad
PCB and circuit design
Schematic
Board
PCB order from JLCPCB
Notes: Kicad Demo

## Slide 29: Good to know – ESP
WiFi capable microcontroller
Bluetooth or WiFi
Dev boards

## Slide 30: Good to know – Raspberry pi
COMPUTER, not microcontroller
Linux system
GPIO pins
Complex logic – written in any language

## Slide 31: How to build at home?
Github repo
BOM – buy
3D model – print (or make it from wood)
Code!
Buy other stuff and experiment!
https://github.com/KerteszDomokos/robotcar-workshop

## Slide 32: Thanks! Ask me! kerteszdomokos@gmail.com